## Slide 1: IoT Challenge 2018- Clustering and Twitter flows Intro
16-17 March 2018

## Slide 2: Clustering flow
Objective: implement a simple generic L architecture in Node-RED
Specific example: Exploit street speed data from Madrid and group speeds in two states (good and bad state)
Store and process, extract high and low speed clusters for a single point
Can be generalized for all points, extended to use a database or used in a different data source

## Slide 3: Clustering flow
Exploit open street data from madrid
  http://informo.munimadrid.es/informo/tmadrid/pm.xml
  Be careful, not all PMs have speed (velocidad field) in them

## Slide 4: Clustering flow horizontal L architecture
Http GET call to Madrid for data
Transformation from XML to JSON
Filter to get only the point we need
  Check returned JSON from Madrid for the structure of the data!!
Transform to csv and store in file

## Slide 5: Clustering flow- Vertical part
Usage of external node.js function ‘clusters’ in kmeans cluster function node
  Be sure to include it in settings.js file
This needs data inserted in a specific form
  Array of arrays of data points
  [[ 2,4],[3,5]…]
Data points come as array of objects from csv file
  Transformed in array of arrays in the split-filter-join part of the flow
Read file produced from the previous flow

## Slide 6: Object to array code in filter function node
If more dimensions are needed in the clustering case, one can add more points in the array

## Slide 7: Clustering flow- diagonal part
Retrieve real time value and compare with cluster centroids
  Current value is already extracted from the horizontal flow
Current value

## Slide 8: Intercept and compare function
var velocity=msg.payload.velocidad; localclusters=global.get("foundclusters"); var overall_cluster=-1; var diff; var min=10000000; for (var k=0;k<localclusters.length;k++){ diff=Math.abs(localclusters[k].centroid[0]-velocity); if (diff<min){ overall_cluster=k; min=diff; } console.log(diff)); } if (overall_cluster===0){ msg.payload="bad state"; } if (overall_cluster===1){ msg.payload="good state"; } msg.payload.cluster_number=overall_cluster; return msg;

## Slide 9: Overall flow

## Slide 10: Twitter count per location flow
Dependencies
  https://github.com/ttezel/twit
  To be added in settings.js

## Slide 11: Twitter count per location flow
Functionalities
  Register in Twitter Streaming API (needs credentials from a Twitter account inside the Twitlib function node)
  REST Service to register a location bounding box for monitoring
    http://localhost:1880/PostBox
  REST Service to get current counters for all bounding boxes
    http://localhost:1880/counters
  REST Service to delete a bounding box from monitoring
    http://localhost:1880/deleteBox